## Slide 1
Department of Mechanical Engineering
B.Tech Project Presentation on
VOLLEY: Controlled CubeSat Deployment
from a Hosted Orbital Platform
Gen5 computational feasibility review
Presented By
Adityavardhan Mishra · Pratham Chawla
PRN 23070125054 · PRN 23070125029
Guide: Vikas Gulia
Review candidate: 19 October 2026
SYMBIOSIS INSTITUTE OF TECHNOLOGY PUNE
1

## Slide 2
Presentation route
OUTLINE
PRESENTATION GUIDE
User-specified final-review outline
2
01 Introduction
02 Literature review
03 Research gap
04 Objectives
05 Research methodology
06 Timeline
07 Work progress
08 Results
09 Conclusion
10 Future work
11 References

## Slide 3
Which missions might value orbital choice?
INTRODUCTION
GEN5 MODEL STUDY
NASA 2026 Small Spacecraft SoA; local market audit; STEP-derived Gen5 CAD
3
Repeat fleets
Configurable satellite fleets exist; demand for VOLLEY is unconfirmed.
Delivery buyer
A carrier or fleet operator might seek several release states from one host.
STEP-derived Gen5 reference; side-fed placement fails its fit check.
Test on one matched mission against springs, host manoeuvres, transport and onboard propulsion.

## Slide 4
Existing methods solve different parts of the problem
LITERATURE REVIEW
GEN5 MODEL STUDY
JAXA; Foster et al. 2018; Feng et al. 2025; Zhao et al. 2022/2025
4
Approach
Strength
Limit for this thesis
Spring deployer
Flight heritage; compact; simple
Limited tailored release speed
Spring release / drag
Relative state or drag can create phasing
Timing alone, with no relative state change, cannot
Orbital transfer vehicle
Larger orbit changes
Greater bus, mass and integration burden
Electromagnetic research
Commandable acceleration studied
Armature, high-g or maturity constraints vary

## Slide 5
A narrower, testable contribution
RESEARCH GAP
GEN5 MODEL STUDY
Thesis manuscript, Related Work and Introduction
5
Commanded release for an unmodified CubeSat at moderate acceleration, with the full system counted.
Contribution examined
Gen5 reusable-sled linear motor, 3U payload, magazine, pulse power, arrest and orbital utility.
Boundary
Electromagnetic CubeSat deployment exists in prior work. Payload qualification and physical performance remain unproved.

## Slide 6
The analytical research objectives have outcomes
OBJECTIVES
GEN5 MODEL STUDY
Thesis manuscript, BASELINE.md and PROVENANCE.md; presentation synthesis
6
Research objective
Final thesis outcome
Design a commandable 3U system
Reference CAD and subsystem concepts documented; feed remains open
Calculate shot and control performance
Historical model completed; finite force screen challenges its rating
Evaluate orbital utility
Conditional orbit results; real lifetime unvalidated
Count full installed burden
Mass rollup completed; 3U parity criterion failed
Test credibility of key claims
Numerical cross-checks and limits recorded

## Slide 7
The analysis chain from mission to decision
RESEARCH METHODOLOGY
GEN5 MODEL STUDY
Thesis manuscript, Models and Verification; validation register
7
Mission & payload needs
→
Architecture trade
→
CAD & mass model
→
Shot, power & orbit models
→
Numerical cross-checks
→
Sensitivity & acceptance bands
Models were challenged and revised; hardware performance remains outside this thesis's evidence.

## Slide 8
Numerical checks changed the review baseline
RESEARCH METHODOLOGY
GEN5 MODEL STUDY
VOLLEY-thesis/appendix/PROVENANCE.md; validation run sheets
8
Question
Method / cross-check
Evidence limit
Field and thrust
Analytic; 2-D FEM; independent 3-D numerical force
Shared ideal inputs; no motor measurement
Shot and power
Dynamics; Monte Carlo; ngspice
Assumed components and interfaces
Structure and flow
CAD; CalculiX; OpenFOAM
No payload qualification
Orbital change
Orbit model; Cowell / GMAT cases
Lifetime depends on atmosphere

## Slide 9
Project evolution: documented decisions and analysis
TIMELINE
GEN5 MODEL STUDY
VOLLEY-thesis/appendix/HISTORY.md; thesis README; PLAN-R2
9
2023
Hosted concept
Free-flyer concept reframed around a host platform
Mid-2025*
LSM direction
Coilgun study gives way to a linear synchronous motor
2025–26*
CAD generations
Geometry and mass models mature through Gen5
Jul–Sep 2026
Gen5 evidence
Cross-checks, defect corrections and thesis record
Oct 2026
Final review
Gen5 results, failed criteria and thesis record prepared
* Approximate historical milestone; not a documented semester deadline.

## Slide 10
2026 findings changed the review baseline
TIMELINE
GEN5 MODEL STUDY
HISTORY.md; PROVENANCE.md; thesis manuscript, Limitations
10
Jul
CAD-derived sled mass replaced an optimistic parametric estimate
Aug
Depth-resolved thrust calculation lowered the historical model speed
Aug
Enclosure buildup exposed the full 3U mass penalty
2026
Independent orbit checks rejected a solar-invariance claim
Final
Results and failures retained in the submitted thesis record

## Slide 11
The current review package is assembled and traceable
WORK PROGRESS
GEN5 MODEL STUDY
Thesis README; validation register; STEP view provenance
11
FreeCAD-linked STEP envelope; internal interference is concealed.
Analysis delivered
Shot, circuit, structural, thermal, orbit and alternative-case models.
Evidence delivered
Manuscript, STEP, scripts, numerical checks and defect register.
Fixed computational study with failed design gates; no physical qualification claim.

## Slide 12
Gen5: fixed reference geometry, feeder fit still open
RESULTS
GEN5 MODEL STUDY
FreeCAD Gen5 STEP reference; view provenance and P116
12
• 1.3 m powered stroke; 1.5 m release station
• Reusable 9.45 kg magnet sled
• Two cassettes; twelve 3U satellites
• FreeCAD STEP assembly: side-fed placement clashes
Enclosure hidden for visibility; no fabricated article.

## Slide 13
Historical periodic-model shot: challenged by finite geometry
RESULTS
GEN5 MODEL PREDICTION
Thesis BASELINE.md; F01_shot.png; P117 energy audit
13
16.0 m/s
exit speed
10.07 g
acceleration
2.782 kJ
gross draw
18.8%
net efficiency
P118 challenges 16.0 m/s; P117 reconciles 124.5 J to assumed model terms.

## Slide 14
Independent 3-D check confirms ideal finite-force work
RESULTS
COMPUTATIONAL CROSS-CHECK
P118 analytic; P119 2-D FEM; P121 3-D numerical; P122 gap sensitivity
14
1.042 kJ
Ideal 3-D work: independent surface-charge formulation agrees with P118 under shared inputs.
−13% work
Illustrative 12-to-14 mm magnet gap change; not a measured tolerance or motor rating.
No measured force, selected inverter or demonstrated release speed exists.

## Slide 15
Modelled command precision is narrow; it is unmeasured
RESULTS
GEN5 MODEL PREDICTION
Thesis BASELINE.md; PROVENANCE.md; F03_mc.png
15
0.0274 m/s
3σ exit-velocity dispersion at a 15.8 m/s fleet setpoint.
Evidence limit
Monte Carlo under modelled sensing and plant tolerances; no measured dispersion.

## Slide 16
Historical orbit input has a separate geometry check
RESULTS
GEN5 TWO-BODY CHECK
P115 Cartesian orbit check; manuscript Astrodynamic Utility
16
+28.8008 km
Immediate two-body axis rise for an assumed historical 16.029 m/s input.
1.602 model
P134 checks the shared static atmosphere; actual lifetime and achieved release remain unvalidated.
Persistent phasing requires a relative state change; this result concerns orbital energy.

## Slide 17
Gen5 fails its 3U mass comparison
RESULTS
GEN5 MODEL STUDY
Thesis manuscript, Payload Class and Mass-per-Satellite; A46 enclosure result
17
Modeled dry mass, 12 slots
126.6 kg
Gen5 per 3U
10.55 kg
Spring comparator
~6 kg
1.76× heavier per 3U payload; the preset 15% parity band fails.

## Slide 18
The current side-fed assembly fails a geometric fit check
RESULTS
CAD INTERFERENCE • OPEN
FreeCAD Gen5 Review.FCStd; P116 assembly packaging report
18
11 mm short
537 mm of track and cassette width inside 526 mm of usable enclosure width.
32,915 mm³
Cassette/track clash per side. Full audit: 17 intersecting pairs, including sled/track and sled/stator.
Reference placement only: a new feeder or enclosure would need a new configuration and rerun.

## Slide 19
R1 clears cassette width, but still has assembly clashes
RESULTS
UNSELECTED GEOMETRY
FreeCAD R1 STEP candidate; exact-solid route ledger
19
12 / 12
Selected scripted 3U paths clear; a whole-assembly audit still finds five intersecting solid pairs.
570 mm
Wider enclosure; 0.5° assumed alignment stack fails its 5 mm gap; lift and retention still open.
Separate R1 candidate; no change to evaluated Gen5 shot, mass or host-fit claims.

## Slide 20
Computed results: from force to mission decision
RESULTS
CAPTURED COMPUTATIONAL RESULTS
P118–P127 finite force, source, tolerance and arrest; matched reference
20
1. Finite-force geometry screen
2. Matched mission screen
→
P125: single-string source power fails at the older commercial ESR bound; no twelve-shot case closes.

## Slide 21
Matched reference mission finds no twelve-shot closure
RESULTS
BOUNDED MISSION SCREEN
Common-input spring/Gen5 study; 100 N host, 450 km, 12 × 4 kg payloads
21
+52.7 kg
One-event device plus resized fuel: Gen5 exceeds spring despite an ideal 1.87 kg fuel saving (P123).
4 / 1 / 1
Accepted twelve-shot prefixes: spring, finite Gen5, historical Gen5.
Assumed host and devices; optimizer result is not an infeasibility proof or product advantage.

## Slide 22
This Gen5 configuration does not pass selection
CONCLUSION
GEN5 MODEL STUDY
Thesis conclusion; P116; matched mission; STEP view provenance
22
• Historical 16.0 m/s is challenged; ideal 12.448 m/s lacks a sourceable single-string bank.
• The modeled system is 76% heavier per 3U customer and the evaluated side-fed CAD clashes.
• R1 retains sled/track and sled/stator clashes; its assumed 0.5° gap stack fails.
• No matched twelve-shot reference closes; Gen5 is a documented negative design study.
STEP reference, enclosure hidden; fit fails. No physical test.

## Slide 23
Gen6 has a testable mission, but no selected article
FUTURE WORK
GEN6 SCREEN • NOT ACHIEVED
P130 matched four-release J2 screen; P131–P132 first-article bounds
23
Matched mission
Two 1U + two 3U targets: both release choices reach ideal states. Assumed device + fuel favors springs by 10.72 kg.
First-article gap
Two STEP envelopes exist; ~9.35 kg remains for all omitted hardware under a surrogate parity screen.
1 km/s remains separate long-range research; no command range or motor rating established.

## Slide 24
Paired cells improve the nominal acceleration path
FUTURE WORK
GEN6 GEOMETRY • UNSELECTED
FreeCAD/STEP R0 packaging comparison; no feeder mechanism selected
24
Staggered
Last cell: 330 mm to brake; 5.56 g ideal mean for 6 m/s.
Paired
At least 900 mm per cell; 2.04 g largest ideal mean at 6 m/s.
26 nominal FreeCAD/STEP states pass represented-solid checks; locks, contact, docking and host fit remain open.

## Slide 25
Next milestone: close G0 and G1 before any build
FUTURE WORK
GEN6 PLAN • NOT ACHIEVED
P130–P132; G0/G1 review gates; no construction authorization
25
Specify
Real customer targets, tolerances and provider interface
Decide
Complete motor, source, brake, contact and installed BOM
Measure
Field, contact, release, arrest, loads and cycle behavior
Review
Drawings, BOM, procedures, uncertainty and review decision

## Slide 26
Core literature and standards (1/2)
REFERENCES
SOURCE LIST
Bibliography from VOLLEY-thesis/source/paper.tex
26
• [1] JAXA, JEM Payload Accommodation Handbook, Vol. 8: Small Satellite Deployment ICD.
• [2] Cal Poly, CubeSat Design Specification, Rev. 14, 2020.
• [3] C. Foster et al., ‘Constellation phasing with differential drag on Planet Labs satellites,’ J. Spacecraft Rockets 55(2), 2018.
• [4] H. Feng et al., ‘Design and reachable domain analysis of on-orbit electromagnetic launcher for CubeSats,’ Int. J. Aerospace Eng., 2025.
• [5] Y. Zhao et al., ‘Design and analysis of a new deployer for the in-orbit release of multiple stacked CubeSats,’ Remote Sensing 14(17), 4205, 2022.

## Slide 27
Methods and project records (2/2)
REFERENCES
SOURCE LIST
Bibliography from VOLLEY-thesis/source/paper.tex; project records
27
• [6] Y. Zhao et al., ‘Simulation analysis and experimental verification of the transport characteristics of a high-volume CubeSat storage device,’ Aerospace 12(6), 466, 2025.
• [7] K. Halbach, ‘Design of permanent multipole magnets with oriented rare earth cobalt material,’ Nucl. Instrum. Methods 169, 1980.
• [8] NASA, General Environmental Verification Standard (GEVS), GSFC-STD-7000A, 2013.
• [9] D. A. Vallado, Fundamentals of Astrodynamics and Applications, 4th ed., 2013.
• [10] A. Mishra, VOLLEY-thesis: manuscript, baseline, provenance and validation records, repo head b30ffdc, 28 Sep 2026.
• [11] VOLLEY, Gen6 G0 mission and article requirements, 12 Oct 2026 (study requirements).

## Slide 28
What the reconciled numerical record establishes
EVIDENCE APPENDIX
MODEL EVIDENCE ONLY
P133/P134 · technical evidence revision, 16 October 2026
28
1.602 model ratio
Separate integration, same static atmosphere. Actual lifetime is unvalidated.
Failures retained
22 Gen5/R1 intersections classified; 126.562 kg model; no sampled twelve-shot mission closes.

## Slide 29
Native solvers: agreement and unresolved differences
EVIDENCE APPENDIX
ORBITAL ANALYSIS
Orekit 13.1.6 / GMAT R2026a; 18 October evidence supplement
29
Prescribed states; no release-accuracy or hardware validation. J2 frames are not harmonized.

## Slide 30
Archived campaign: sampled proximity has a limit
EVIDENCE APPENDIX
GMAT R1 ARCHIVE
Twelve preloaded post-release orbits; simulation dates in 2027
30
190.15 m sampled; 180.29 m interpolated. Continuous clearance remains unproven.

## Slide 31
The J2 setup discrepancy now has a bounded resolution
EVIDENCE APPENDIX
NUMERICAL CONSISTENCY
GMAT R2026a / Orekit 13.1.6 · matched prescribed pole, 19 October
31
1.285 mm maximum over one day. Shared orientation; no physical orbit or release-accuracy claim.

## Slide 32
Precise delivery needs a measured control budget
FUTURE-WORK APPENDIX
GEN6 SURROGATE
CNR-01 · complete native event replay and deterministic sensitivity
32
+0.1% imposed release-speed bias gives ~1.53 km error. Numerical agreement is not flight precision.

## Slide 33
Seven feeder concepts: inspectable geometry, open hardware gates
FUTURE-WORK APPENDIX
UNSELECTED CANDIDATES
Native FreeCAD / STEP · analytical cases / CalculiX fixture · 19 October
33
• 1U/3U CAD and bounded motion checks
• Load, tolerance and fault cases retained
• Arrest-tooth sizing fails adverse cases
• Handoff, latch engagement and installed parts unverified
• No baseline selection or hardware release
STEP-derived orthographic view; no measured reliability or full-cycle qualification.

## Slide 34
Native mesh and result view: keep the fixture explicit
EVIDENCE APPENDIX
ASSUMED CLAMPED FLOOR
CalculiX2.23 DAT / INP displayed in Gmsh4.14.1 · undeformed geometry
34
Displacement norm in metres. Actual joints absent; peak support stress is not converged or a strength pass.

## Slide 35
Continuous feed geometry exposes the remaining safety work
FUTURE-WORK APPENDIX
PRESCRIBED MOTION ONLY
CT-01 · separate captive-transfer coupon; 19 October 2026
35
• 20 continuous 1U/3U phase checks
• Downward gate needs under-deck volume
• Stop travel and adverse fit cases fail
• Real latch/custody and drive remain open
Native CAD and nominal translation proof do not establish full mechanism safety or a selected feeder.

## Slide 36
Orbital reload: define the interface before promising a service
FUTURE-WORK APPENDIX
BASELINE OPERATIONAL NO-GO
RPL-01 · limited cooperative-cartridge feasibility
36
108 capture / 36 fit sensitivities. No integrated reload mechanism; ground loading remains the assumption.